## Slide 1: Nvidia GTX480 Design and Heat Dissipation Trend Exploration Qiyu Chen, Junzhe Huang
EECS - Computer Science and Engineering
Dec 8, 2022

## Slide 2: Overview
Tools and methodologies
Experimental results and technical insights
Qualitative summary

## Slide 3: Tools and methodologies
Tools:
  GPGPU-Sim [1]
  HotSpot [2]
  Conda
Methodologies:
  CUDA kernels design: MatMul and Needleman-Wunsch
  GPU design: a 4-layer, 3D GTX480 floor plan
  Heat dissipation analysis with different
    kernel operations
    tensor size
  Heatmap visualization
[1] https://github.com/gpgpu-sim/gpgpu-sim_distribution
[2] https://www.cs.virginia.edu/rodinia/doku.php

## Slide 4: Experimental results
Input tensor sizes:
  MatMul: 50, 100, 200, 300, 400
  Needleman-Wunsch: 128, 192, 256, 320, 384
Outputs (along with corresponding input tensor sizes):
  3D floor plan configurations based on Fermi architecture
  Heatmaps for all 4 layers and 2 operations
  Power logs for 2 operations:
    Average
    Max
    Min
  Automation script to make it a one-click system

## Slide 5: Experimental results
Heatmaps

## Slide 6: Experimental results
Power traces

## Slide 7: Experimental results
Automation script

## Slide 8: Summary
MatMul takes longer time to run
The average power consumption of MatMul is higher than that of NW. Both power traces show downward trends when input tensor sizes increases
  except the power of MatMul when input size is fairly small (50), which is 51.402w (compared to 100.178w when input size is 100)
The average and maximum temperatures of NW are obviously higher than MatMul